## Slide 1: Hardware
IGCSE Computer Science (0478) – Chapter 3 Detailed Presentation

## Slide 2: Chapter Overview
Input Devices
Output Devices
Storage Devices (Primary, Secondary, Offline)
Von Neumann Architecture

## Slide 3: What Are Input Devices?
Hardware that sends data to a computer for processing.
Manual (human‑operated) and automatic (sensor‑based) devices.

## Slide 4: Manual Input Devices
Keyboard – text entry, command shortcuts
Mouse / Touchpad – pointer control and selection
Touchscreen – direct finger/stylus input
Graphics Tablet – precision drawing for designers
Game Controller / Joystick – gaming and simulations

## Slide 5: Automatic Input Devices
Scanner – digitises images or documents
Barcode & QR Scanner – retail, inventory
OCR / OMR / MICR – reading printed text/marks/cheques
Digital Camera & Webcam – photo, video
Microphone – voice commands, VoIP
Sensors (temperature, motion, light) – IoT & robotics

## Slide 6: What Are Output Devices?
Hardware that receives data from a computer and presents it to users.

## Slide 7: Visual Output
Monitor / Display (LCD, LED, OLED) – graphical interface
Projector – large‑scale presentations
VR / AR Headset – immersive environments

## Slide 8: Printed Output
Inkjet Printer – affordable colour photos
Laser Printer – fast, high‑volume text
3D Printer – additive manufacturing of prototypes

## Slide 9: Audio & Haptic Output
Speakers & Headphones – music, alerts
Actuators – motors controlling robots, drones
Haptic Devices – vibration feedback in gaming controllers

## Slide 10: Storage Categories
Primary Storage – directly accessible by CPU (RAM, ROM)
Secondary Storage – internal mass storage (HDD, SSD)
Offline / Removable – optical discs, USB flash, external drives

## Slide 11: Primary Storage
RAM (Random Access Memory): volatile, temporary workspace
• DRAM for main memory, SRAM for CPU cache
ROM (Read‑Only Memory): non‑volatile, stores firmware/boot code

## Slide 12: Magnetic Storage – HDD
Platters coated with magnetic material spin at 5 400–15 000 RPM
Read/Write heads hover nanometres above platters
Data stored in tracks and sectors as magnetic polarity
Pros: multi‑TB capacity, low cost per GB
Cons: mechanical wear, shock‑sensitive, slower than SSD

## Slide 13: How an HDD Works
1. Platters spin inside sealed enclosure
2. Actuator positions the head over desired track
3. Head magnetises tiny domains (write) or senses polarity (read)
4. Controller translates magnetic changes into binary data

## Slide 14: Solid‑State Storage – SSD / Flash
Uses NAND flash memory with no moving parts
Data stored as charge in floating‑gate transistors
Fast access (SATA ~550 MB/s, NVMe >3 GB/s)
Silent, shock‑resistant, lower latency, higher cost per GB

## Slide 15: How an SSD Works
1. Data written as electrons trapped in floating gate (0/1)
2. Pages grouped into blocks; whole blocks erased before rewrite
3. Controller manages wear‑levelling & error correction
4. TRIM command cleans unused blocks to maintain speed

## Slide 16: Optical Storage – CD / DVD / Blu‑ray
Data encoded as pits and lands on disc surface
Laser reflects differently from pits vs lands (binary)
Capacities: CD 700 MB, DVD 4.7 GB, Blu‑ray 25 GB
Cheap distribution, good archival life, slower and fragile

## Slide 17: How Optical Discs Work
1. Disc spins while laser focuses on spiral track
2. Reflected light intensity changes at pits
3. Sensor converts reflections into digital data for CPU

## Slide 18: Storage Comparison Highlights
Speed: SSD > HDD >> Optical
Capacity: HDD (multi‑TB) > SSD > Optical
Cost per GB: HDD cheapest, SSD moderate, Optical highest
Durability: SSD robust, HDD mechanical, Optical scratch‑sensitive

## Slide 19: Von Neumann Architecture
Stored‑program computer model used by most CPUs
Components: CPU (ALU + Control Unit), Memory, Input/Output, Buses
Buses: Address, Data, Control – carry signals between components

## Slide 20: Fetch–Decode–Execute Cycle
1. Fetch: PC address placed on Address Bus to memory; instruction loaded to MDR
2. Decode: Control Unit interprets opcode
3. Execute: ALU or relevant unit performs operation; results stored
Registers: PC, MAR, MDR, ACC, CIR

## Slide 21: Key Takeaways
Wide range of input & output devices enable human‑computer interaction
Storage choice balances speed, capacity, cost, durability
Von Neumann architecture underpins modern computing
Understanding hardware is essential for selecting and troubleshooting systems